## Slide 1: GPU Computing Architecture
HiPEAC Summer School, July 2015
Tor M. Aamodt
aamodt@ece.ubc.ca
University of British Columbia
NVIDIA Tegra X1 die photo
/

## Slide 2: SIMT Execution Model
Programmers sees MIMD threads (scalar)
GPU bundles threads into warps (wavefronts) and runs them in lockstep on SIMD hardware
An NVIDIA warp groups 32 consecutive threads together (AMD wavefronts group 64 threads together)
Aside: Why “Warp”? In the textile industry, the term “warp” refers to “the threads stretched lengthwise in a loom to be crossed by the weft” [Oxford Dictionary].
[https://en.wikipedia.org/wiki/Warp_and_woof]
Notes: MIMD = multiple-instruction, multiple-data

## Slide 3: SIMT Execution Model
Challenge: How to handle branch operations when different threads in a warp follow a different path through program?
Solution: Serialize different paths.
A: v = foo[threadIdx.x];
B: if (v < 10)
C: v = 0;
else
D: v = 10;
E: w = bar[threadIdx.x]+v;
Time
A
T1
T2
T3
T4
B
T1
T2
T3
T4
C
T1
T2
D
T3
T4
E
T1
T2
T3
T4
foo[] = {4,8,12,16};
Notes: MIMD = multiple-instruction, multiple-data

## Slide 4: GPU Memory Address Spaces
GPU has three address spaces to support increasing visibility of data between threads: local, shared, global
In addition two more (read-only) address spaces: Constant and texture.

## Slide 5: Local (Private) Address Space
Each thread has own “local memory” (CUDA) “private memory” (OpenCL).
0x42
Note: Location at address 100 for thread 0 is different from location at address 100 for thread 1.
Contains local variables private to a thread.

## Slide 6: Global Address Spaces
thread block X
thread block Y
Each thread in the different thread blocks (even from different kernels) can access a region called “global memory” (CUDA/OpenCL).
Commonly in GPGPU workloads threads write their own portion of global memory. Avoids need for synchronization—slow; also unpredictable thread block scheduling.
0x42

## Slide 7: Shared (Local) Address Space
Each thread in the same thread block (work group) can access a memory region called “shared memory” (CUDA) “local memory” (OpenCL).
Shared memory address space is limited in size (16 to 48 KB).
Used as a software managed “cache” to avoid off-chip memory accesses.
Synchronize threads in a thread block using __syncthreads();
thread block
0x42

## Slide 8: Review: Bank Conflicts
To increase bandwidth common to organize memory into multiple banks.
Independent accesses to different banks can proceed in parallel
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 
Example 1: Read 0, Read 1
(can proceed in parallel)
Example 2: Read 0, Read 3
(can proceed in parallel)
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 
Example 3: Read 0, Read 2
(bank conflict)
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 

## Slide 9: Shared Memory Bank Conflicts
__shared__ int A[BSIZE];
…
A[threadIdx.x] = … // no conflicts
0 | 
32 | 
64 | 
96 | 
1 | 
33 | 
65 | 
97 | 
31 | 
63 | 
95 | 
127 | 
2 | 
34 | 
66 | 
98 | 

## Slide 10: Shared Memory Bank Conflicts
__shared__ int A[BSIZE];
…
A[2*threadIdx.x] = // 2-way conflict
0 | 
32 | 
64 | 
96 | 
1 | 
33 | 
65 | 
97 | 
31 | 
63 | 
95 | 
127 | 
2 | 
34 | 
66 | 
98 | 

## Slide 11: CUDA Streams
CUDA (and OpenCL) provide the capability to overlap computation on GPU with memory transfers using “Streams” (Command Queues)
A Stream orders a sequence of kernels and memory copy “operations”.
Operations in one stream can overlap with operations in a different stream.

## Slide 12: How Can Streams Help?
Serial:
Streams:
cudaMemcpy(H2D)
kernel<<<>>>
cudaMemcpy(D2H)
http://on-demand.gputechconf.com/gtc-express/2011/presentations/StreamsAndConcurrencyWebinar.pdf
cudaMemcpy(H2D)
K0
DH0
K1
DH1
K2
DH2
Time
Savings
GPU idle
GPU idle
GPU busy

## Slide 13: Recent Features in CUDA
Dynamic Parallelism (CUDA 5): Launch kernels from within a kernel. Reduce work for e.g., adaptive mesh refinement.
Unified Memory (CUDA 6): Avoid need for explicit memory copies between CPU and GPU
http://devblogs.nvidia.com/parallelforall/unified-memory-in-cuda-6/
See also, Gelado, et al. ASPLOS 2010.

## Slide 14: GPU Instruction Set Architecture (ISA)
NVIDIA defines a virtual ISA, called “PTX” (Parallel Thread eXecution)
More recently, Heterogeneous System Architecture (HSA) Foundation (AMD, ARM, Imagination, Mediatek, Samsung, Qualcomm, TI) defined the HSAIL virtual ISA.
PTX is Reduced Instruction Set Architecture (e.g., load/store architecture)
Virtual: infinite set of registers (much like a compiler intermediate representation)
PTX translated to hardware ISA by backend compiler (“ptxas”). Either at compile time (nvcc) or at runtime (GPU driver).

## Slide 15: Some Example PTX Syntax
Registers declared with a type:
.reg .pred p, q, r;
.reg .u16 r1, r2;
.reg .f64 f1, f2;
ALU operations
add.u32 x, y, z; // x = y + z
mad.lo.s32 d, a, b, c; // d = a*b + c
Memory operations:
ld.global.f32 f, [a];
ld.shared.u32 g, [b];
st.local.f64 [c], h
Compare and branch operations:
setp.eq.f32 p, y, 0; // is y equal to zero?
@p bra L1 // branch to L1 if y equal to zero

## Slide 16: Part 2: Generic GPGPU Architecture

## Slide 17: Extra resources
GPGPU-Sim 3.x Manualhttp://gpgpu-sim.org/manual/index.php/GPGPU-Sim_3.x_Manual

## Slide 18: GPU Microarchitecture Overview
Single-Instruction, Multiple-Threads
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 19: GPU Microarchitecture
Companies tight lipped about details of GPU microarchitecture.
Several reasons:
  Competitive advantage
  Fear of being sued by “non-practicing entities”
  The people that know the details too busy building the next chip
Model described next, embodied in GPGPU-Sim, developed from: white papers, programming manuals, IEEE Micro articles, patents.

## Slide 20
GPGPU-Sim v3.x w/ SASS
Correlation
~0.976
12
Chart: HW - GPGPU-Sim Comparison

## Slide 21: GPU Microarchitecture Overview
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 22: Inside a SIMT Core
SIMT front end / SIMD backend
Fine-grained multithreading
  Interleave warp execution to hide latency
  Register values of all threads stays in core
SIMT
Front End
SIMD Datapath
Fetch
Decode
Schedule
Branch
Memory Subsystem
Icnt.
Network
SMem
L1 D$
Tex $
Const$
Reg
File

## Slide 23: Inside an “NVIDIA-style” SIMT Core
SIMT Front End
SIMD Datapath
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
Three decoupled warp schedulers
Scoreboard
Large register file
Multiple SIMD functional units
Scheduler 1
Scheduler 2
Scheduler 3

## Slide 24: Fetch + Decode
Arbitrate the I-cache among warps
  Cache miss handled by fetching again later
Fetched instruction is decoded and then stored in the I-Buffer
  1 or more entries / warp
  Only warp with vacant entries are considered in fetch
Inst. W1
r
Inst. W2
Inst. W3
v
r
v
r
v
To
Fetch
Issue
Decode
Score-
Board
Issue
ARB
PC
1
PC
2
PC
3
A
R
B
Selection
T
o
I
-
C
a
c
h
e
Valid[1:N]
I-Cache
Decode
I-Buffer
Fetch
Valid[1:N]

## Slide 25: Instruction Issue
Select a warp and issue an instruction from its I-Buffer for execution
  Scheduling: Greedy-Then-Oldest (GTO)
  GT200/later Fermi/Kepler: Allow dual issue (superscalar)
  Fermi: Odd/Even scheduler
  To avoid stalling pipeline might
  keep instruction in I-buffer until
  know it can complete (replay)

## Slide 26: Review: In-order Scoreboard
Scoreboard: a bit-array, 1-bit for each register
  If the bit is not set: the register has valid data
  If the bit is set: the register has stale data
    i.e., some outstanding instruction is going to change it
Issue in-order: RD  Fn (RS, RT)
  If SB[RS] or SB[RT] is set  RAW, stall
  If SB[RD] is set  WAW, stall
  Else, dispatch to FU (Fn) and set SB[RD]
Complete out-of-order
  Update GPR[RD], clear SB[RD]
Regs[R1]
Regs[R2]
Regs[R3]
Regs[R31]
1
0
0
0
Register File
Scoreboard
[Gabriel Loh]
+
Notes: H&P-style notation

## Slide 27: Example
- | - | - | -
- | - | - | -
Warp 0
Warp 1
ld r7, [r0]
mul r6, r2, r5
add r8, r6, r7
Index 0
Index 1
Scoreboard
Index 2
Warp 0
Warp 1
Instruction Buffer
i0 i1 i2 i3
Index 3
r7 | - | - | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
r7 | r6 | - | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 1 | 0 | 0
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 1 | 0 | 0
r7 | r6 | r8 | -
- | - | - | -
r7 | r6 | r8 | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 0 | 0 | 0
r7 | - | r8 | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 0 | 0 | 0
r7 | - | r8 | -
- | - | - | -
add r8, r6, r7 | 0 | 0 | 0 | 0
- | - | r8 | -
- | - | - | -
Code
+

## Slide 28: SIMT Using a Hardware Stack
-
G
1111
TOS
B
C
D
E
F
A
G
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B/1111
C/1001
D/0110
E/1111
A/1111
G/1111
-
A
1111
TOS
E
D
0110
E
C
1001
TOS
-
E
1111
E
D
0110
TOS
-
E
1111
A
D
G
A
Time
C
B
E
-
B
1111
TOS
-
E
1111
TOS
Reconv. PC
Next PC
Active Mask
Stack
E
D
0110
E
E
1001
TOS
-
E
1111
Stack approach invented at Lucafilm, Ltd in early 1980’s
SIMT = SIMD Execution of Scalar Threads
Version here from [Fung et al., MICRO 2007]

## Slide 29: Register File
32 warps, 32 threads per warp, 16 x 32-bit registers per thread = 64KB register file.
Need “4 ports” (e.g., FMA) greatly increase area.
Alternative: banked single ported register file. How to avoid bank conflicts?

## Slide 30: Banked Register File
Strawman microarchitecture:
Register layout:

## Slide 31: Register Bank Conflicts
warp 0, instruction 2 has two source operands in bank 1: takes two cycles to read.
Also, warp 1 instruction 2 is same and is also stalled.
Can use warp ID as part of register layout to help.

## Slide 32: Operand Collector
Term “Operand Collector” appears in figure in NVIDIA Fermi Whitepaper
Operand Collector Architecture (US Patent: 7834881)
  Interleave operand fetch from different threads to achieve full utilization
Bank 0
Bank 1
Bank 2
Bank 3
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
…
…
…
…
add.s32 R3, R1, R2;
No Conflict
mul.s32 R3, R0, R4;
Conflict at bank 0

## Slide 33: Operand Collector (1)
Issue instruction to collector unit.
Collector unit similar to reservation station in tomasulo’s algorithm.
Stores source register identifiers.
Arbiter selects operand accesses that do not conflict on a given cycle.
Arbiter needs to also consider writeback (or need read+write port)

## Slide 34: Operand Collector (2)
Combining swizzling and access scheduling can give up to ~ 2x improvement in throughput

## Slide 35: Warp Scheduling Basics

## Slide 36: Loose Round Robin (LRR)
Goes around to every warp and issue if ready (R)
If warp is not ready (W), skip and issue next ready warp
Issue: Warps all run at the same speed, potentially all reaching memory access phase together and stalling.
R
R
W
R
R
R
R
Select
All Warps
Execution Units
W
. . .

## Slide 37: Two-level (TL)
Warps are grouped into two groups:
  Pending warps (potentially waiting on long latency instr.)
  Active warps (Ready to execute)
  Warps move between Pending and Active groups
Within the Active group, issue LRR
Goal: Overlap warps performing computation with warps performing memory access
P
P
P
P
P
P
P
A
A
A
A
Select
Pending Warps
Active Warps
Execution Units
P
. . .
. . .

## Slide 38: Greedy-then-oldest (GTO)
Schedule from a single warp until it stalls
Then pick the oldest warp (time warp assigned to core)
Goal: Improve cache locality for greedy warp
R
R
W
R
R
R
R
Select
All Warps
Execution Units
W
. . .

## Slide 39
Cache-Conscious Wavefront Scheduling
Timothy G. Rogers1
Mike O’Connor2
Tor M. Aamodt1
1The University of British Columbia
2AMD Research

## Slide 40
Compute Unit
DRAM
DRAM
Wavefronts and Caches
Threads in Wavefront
Compute Unit
W1
…
…
Wavefront Scheduler
W2
DRAM
…
10’s of thousands concurrent threads
High bandwidth memory system
Include data caches
…
ALU
ALU
ALU
…
…
L2 cache
Memory Unit
L1D
High Level Overview of a GPU

## Slide 41
Motivation
Improve performance of highly parallel applications with irregular or data dependent access patterns on GPU
These workloads can be highly cache-sensitive
Increase 32k L1D to 8M
  Minimum 3x speedup
  Mean speedup >5x
Breadth First Search (BFS)
K-Means (KMN)
Memcached-GPU (MEMC)
Parallel Garbage Collection (GC)

## Slide 42
Data Cache
Data Cache
Where does the locality come from?
Classify two types of locality
Intra-wavefront locality
Inter-wavefront locality
LD $line (X)
LD $line (X)
LD $line (X)
LD $line (X)
Wave0
Hit
Wave0
Wave1
Hit

## Slide 43
0
20
40
60
80
100
120
AVG-Highly Cache Sensitive
(Hits/Miss) PKI
Misses PKI
Inter-Wavefront Hits PKI
Intra-Wavefront Hits PKI
Quantifying intra-/inter-wavefront locality

## Slide 44
Observation
Issue-level scheduler chooses the access stream
Memory System
Wavefront Scheduler
Wavefront Scheduler
Round Robin Scheduler
Memory System
Greedy then Oldest Scheduler
ld A
,B,C,D…
DC
B
A
ld Z,Y,X,W
ld A,B,C,D
WX
Y
Z
...
...
ld Z,Y,X,W
DC
B
A
DC
B
A
ld A,B,C,D…
...
Wave0
Wave1
Wave0
Wave1
ld A,B,C,D…

## Slide 45
A,B,C,D
E,F,G,H
I,J,K,L
A,B,C,D
E,F,G,H
I,J,K,L
W0
W1
W2
W0
W1
W2
Optimal Replacement using RR scheduler
LRU replacement
A,B,C,D
W0
A,B,C,D
W0
E,F,G,H
W1
E,F,G,H
W1
I,J,K,L
W2
I,J,K,L
W2
A
B
C
D
4 hits
12 hits
E
F
L
Difficult Access Stream
Need a better replacement Policy?

## Slide 46
Why miss rate is more sensitive to scheduling than replacement
…
1024 threads = thousands of memory accesses
…
…
…
1
2
A
Wavefront Scheduler
Replacement Policy
Ld A
Ld A
Ld B
Ld C
Ld C
Ld D
Ld E
Ld E
Ld F
W0
W1
W31
Decision picks from thousands of potential accesses
Decision limited to one of A possible ways
…

## Slide 47
0
10
20
30
40
50
60
70
80
90
AVG-Highly Cache-Sensitive
Does this ever Happen?
Loose Round Robin with LRU
  Belady Optimal
Greedy Then Oldest with LRU
Consider two simple schedulers
MPKI
Chart: MPKI

## Slide 48
Key Idea
Use the wavefront scheduler to shape the access pattern
Memory System
Wavefront Scheduler
Wavefront Scheduler
Greedy then Oldest Scheduler
Memory System
Cache-Conscious Wavefront Scheduler
ld A,B,C,D
DC
B
A
ld Z,Y,X,W
ld A,B,C,D
WX
Y
Z
...
...
ld Z,Y,X,W
DC
B
A
DC
B
A
ld Z,Y,X,W…
ld A,B,C,D…
...
...
ld Z,Y,X,W…
Wave0
Wave1
Wave0
Wave1
ld A,B,C,D…
WX
Y
Z
WX
Y
Z

## Slide 49
Time
CCWS Components
Locality Scoring System
Balances cache miss rate and overall throughput
Lost Locality Detector
W0
W1
W2
W0
W1
W2
Victim Tags
Tag
Tag
Tag
Tag
Tag
Tag
W0
W1
W2
Detects when wavefronts have lost intra-wavefront locality
L1 victim tags organized by wavefront ID
More Details in the Paper
Score

## Slide 50
CCWS Implementation
Memory Unit
Cache
Victim Tags
Locality Scoring System
Wave Scheduler
W0
W1
W2
Tag
WID
Data
Tag
Tag
Tag
Tag
Tag
Tag
W0
W1
W2
Time
Score
Tag
WID
Data
…
W0
W1
W2
No W2 loads
W0
W1
W2
…
W0: ld X
X
0
W0,X
X
W0 detected lost locality
W2: ld Y
W0: ld X
ProbeW0,X
Y
2
More Details in the Paper

## Slide 51
Methodology
GPGPU-Sim (version 3.1.0)
30 Compute Units (1.3 GHz)
  32 wavefront contexts (1024 threads total)
32k L1D cache per compute unit
  8-way
  128B lines
  LRU replacement
1M L2 unified cache
Stand Alone GPGPU-Sim Cache Simulator
Trace-based cache simulator
Fed GPGPU-Sim traces
Used for oracle replacement

## Slide 52
Performance Results
Also Compared Against
A 2-LVL scheduler
  Similar to GTO performance
A profile-based oracle scheduler
  Application and input data dependent
  CCWS captures 86% of oracle scheduler performance
Variety of cache-insensitive benchmarks
  No performance degradation
0
0.5
1
1.5
2
HMEAN-Highly Cache-Sensitive
Speedup
LRR
GTO
CCWS

## Slide 53
0
10
20
30
40
50
60
70
80
90
AVG-Highly Cache-Sensitive
Cache Miss Rate
CCWS less cache misses than other schedulers optimally replaced
Full Sensitivity Study in Paper
MPKI
Chart: MPKI

## Slide 54
Related Work
Wavefront Scheduling
Gerogia Tech - GPGPU Workshop 2010
UBC - HPCA 2011
UT Austin - MICRO 2011
UT Austin/NVIDIA/UIUC/Virginia - ISCA 2011
OS-Level Scheduling
SFU – ASPLOPS 2010
Intel/MIT – ASPLOPS 2012

## Slide 55
Conclusion
Different approach to fine-grained cache management
Good for power and performance
High level insight not tied specifics of a GPU
  Any system with many threads sharing a cache can potentially benefit
Questions?

## Slide 56
Warped Gates: Gating Aware Scheduling
and Power Gating for GPGPUs
Mohammad Abdel-Majeed* Daniel Wong*
Murali Annavaram
Ming Hsieh Department of Electrical Engineering
University of Southern California
MICRO-2013
* Equal Contribution
Supported by

## Slide 57: Problem Overview
Execution unit accounts for majority of energy consumption in GPGPU, even more than Mem and Reg!
Leakage energy is becoming a greater concern with technology scaling
Traditional microprocessor power gating techniques are ineffective in GPGPUs
Component Energy Breakdown for GTX480[1]
[1] J. Leng, T. Hetherington, A. ElTantawy, S. Gilani, N. S. Kim, T. M. Aamodt, and V. J. Reddi, “GPUWattch: enabling energy optimizations in GPGPUs,” presented at the ISCA '13: Proceedings of the 40th Annual International Symposium on Computer Architecture, 2013.
Overview | 57

## Slide 58: GPGPU Overview (GTX480)
V | Dec_INST | R
V | Dec_INST | R
V | Dec_INST | R
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
SFU
SFU
SFU
SFU
SFU LD/ST SP0 SP1
INT Unit
Operands
Result Queue
FP Unit
Warp Scheduler
(2-level)
Register File
128KB
Execution Units
64KB shared Memory/L1 cache
SM
Instruction Cache
Fetch and decode
I_Buffer
Overview | 58
SP accounts for 98% of Execution Unit Leakage Energy
Execution units account for 68% of total on chip area

## Slide 59: Power Gating Overview
Cuts off leakage current that flows through a circuit block
Power gate at SP granularity
Important Parameters:
  Wakeup Delay – Time to return to Vdd (3 cycles)
  Breakeven Time – # of consecutive power gated cycles required to compensate PG energy overhead (9-24 cycles)
  Idle Detect - # of idle cycles before power gating[2]
Time
Static Energy
t2
t0
t1
t3
t4
Eoverhead
Overhead to sleep
and Wakeup
Overhead to Sleep
Cumulative energy savings
Wakeup
Cycles>wakeup_delay
Uncompensated
Cycle 1
Cycle 1+BET
Cycles>idle_detect
Compensated
Cycles>BET time
Idle_detect
Busy
Overview | 59
Breakeven Time
[2] Z. Hu, et. al. Microarchitectural techniques for power gating of execution units. In ISLPED ’04.

## Slide 60
Power Gating Challenges in GPGPUs
Challenges | 60

## Slide 61: Power Gating Challenges in GPGPUs
Traditional microprocessors experience idle periods many 10s of cycles long[3]
Int. Unit Idle period length distribution for hotspot
  Assume 5 idle detect, 14 BET
Lost Opportunity
Energy Loss or Neutral
Energy Savings
[3] S. Dropsho, et. al. Managing static leakage energy in microprocessor functional units. In Proceedings of the MICRO 35, 2012
Challenges | 61
Need to increase idle period length

## Slide 62: Warp Scheduler Effect on Power Gating
Idle periods interrupted by instructions that are greedily scheduled
INT
FP
FP
INT
INT
FP
INT
Ready Warps
INT
Need to coalesce warp issues by resource type
Challenges | 62
Idle Periods

## Slide 63
GATES:
Gating Aware Two-level Scheduler
Issue warps based on execution unit resource type
GATES | 63

## Slide 64: Gating Aware Two-level Scheduler (GATES)
INT
FP
INT
INT
INT
FP
FP
Ready Warps
INT
GATES | 64
Idle Period
Idle periods are coalesced

## Slide 65: Gating Aware Two-level Scheduler (GATES)
Per instruction type active warps subset
Instruction Issue Priority
Dynamic priority switching
  Switch highest priority when it out of ready warps
Two-level
GATES
GATES | 65

## Slide 66: Effect of GATES on Idle Period Length
~3x increase in positive power gating events
~2x increase in negative power gating events
Need to further stretch idle periods
Two-level
GATES
GATES | 66

## Slide 67
Blackout Power Gating
Forced idleness of execution units to meet BET
Blackout | 67

## Slide 68: Blackout Power Gating
Force idleness until break even time has passed
  Even when there are pending instructions
Would this not cause performance loss?
  No, because of GPGPU-specific large heterogeneity of execution units and good mix of instruction types
Blackout | 68
Wakeup
Cycles>wakeup_delay
Uncompensated
Cycle 1
Cycle 1+BET
Cycles>idle_detect
Compensated
Cycles>BET time
Idle_detect
Busy
X
X

## Slide 69: Blackout Power Gating
~2.4x increase in positive PG events over GATES (GATES ~3x w.r.t. baseline)
GATES
GATES + Blackout
Blackout | 69

## Slide 70: Blackout Policies
Naïve Blackout
  GATES and Blackout is independent
Can lead to overaggressive power gating
Blackout | 70
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
SP0 SP1
Warp Scheduler
(GATES)
Idle Detect
INT
X

## Slide 71: Blackout Policies
Coordinated Blackout
PG only when active warps count = 0
Blackout | 71
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
SP0 SP1
Warp Scheduler
(GATES)
Idle Detect
Dynamic priority switching is Blackout aware
Active Warp Count Based
INT
✓

## Slide 72: Impact of Blackout
Some benchmarks still show poor performance
  Not enough active warps to hide forced idleness
Goal is as close to 0% overhead as possible

## Slide 73
Adaptive Idle Detect
Reducing Worst Case Blackout Impact
Adaptive Idle Detect | 73

## Slide 74: Adaptive Idle Detect
Dynamically change idle detect to avoid aggressive PG
Infer performance loss due to Blackout
  “Critical Wakeup” – Wakeup that occur the moment blackout period ends
High Correlation vs Runtime
Adaptive Idle Detect | 74

## Slide 75: Adaptive Idle Detect
Independent idle detect values for INT and FP pipelines
Break execution time into epoch (1000 cycles)
If critical wakeup > threshold, idleDetect++
Conservatively decrement idleDetect every 4 epochs
Bound idle detect between 5 – 10 cycles
GATES
Blackout
Adaptive Idle Detect
Warped Gates
Adaptive Idle Detect | 75

## Slide 76: Architectural Support
2-bit type indicator
2 counters keep track of number of INT/FP instr in active subset. Used to determine dynamic priority
Architectural Support | 76

## Slide 77
Evaluation
Evaluation | 77

## Slide 78: Evaluation Methodology
GPGPU-Sim v3.0.2
  Nvidia GTX480
GPUWattch and McPAT for Energy and Area estimation
18 Benchmarks from ISPASS, Rodinia, Parboil
Power Gating parameters
  Wakeup delay – 3 cycles
  Breakeven time – 14 cycles
  Idle detect – 5 cycles
Evaluation | 78

## Slide 79: Power Gating Wakeups / Overhead
Coalescing idle periods – fewer, but longer, idle periods
Blackout reduces PG overhead by 26%
Warped Gates reduces PG overhead by 46%
Evaluation | 79

## Slide 80: Integer Unit Static Energy Savings
Blackout/Warped Gates is able to save energy when ConvPG cannot
Warped Gates saves ~1.5x static energy w.r.t. ConvPG
Evaluation | 80

## Slide 81: FP Unit Static Energy Savings
Warped Gates save ~1.5x static energy w.r.t. ConvPG
  (Ignores Integer only benchmarks)
Evaluation | 81

## Slide 82: Performance Impact
Naïve Blackout has high overhead due to aggressive PG
Both ConvPG and Warped Gates has ~1% overhead
Evaluation | 82

## Slide 83: Conclusion
Execution units – largest energy usage in GPGPUs
Static energy becoming increasingly important
Traditional microprocessor power gating techniques ineffective in GPGPUs due to short idle periods
GATES – Scheduler level technique to increase idle periods by coalescing instruction type issues
Blackout – Forced idleness of execution unit to avoid negative power gating events
Adaptive Idle Detect – Limit performance impact
Warped Gates able to save 1.5x more static power than traditional microprocessor techniques, with negligible performance loss
Conclusion | 83

## Slide 84
Thank you!
Questions?
Conclusion | 84