## Slide 1: CS203 – Advanced Computer Architecture
Tomasulo Algorithm
- Superscalar

## Slide 2: Tomasulo Example
Loop: LD R2,0(R1)
DADDIU R2,R2,#1
SD R2,0(R1)
DADDIU R1,R1,#8
BNE R2,R3,LOOP
Assumption:
Add/Branch – 1 cycle
Load/Store – 2 cycles
(Addr. Gen & Mem. Access)
*Assume 2-issue superscalar
2 instruction can commit/clock
(2 CDB)
Branch
FP Adder
Memory

## Slide 3
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 |  |  |  |  |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Store1 |  |  |  |  |  |  | 
Store2 |  |  |  |  |  |  | 
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) |  |  |  |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 |  |  |  |  |  | (R2) = 6
1 | SD R2, 0(R1) |  |  |  |  |  | Mem[100] = 6
1 | DADDIU R1, R1, #8 |  |  |  |  |  | (R1) = 108
1 | BNE R2, R3, LOOP |  |  |  |  |  | 6 ≠ 10
2 | LD R2, 0(R1) |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  | 7 ≠ 10
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 4
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 | 1 | ADD |  | 1 | Load1 |  | 
Add2 |  |  |  |  |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 |  |  |  |  |  |  | 
Load1 | 1 | LD | 100 |  |  |  | 0
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Store1 |  |  |  |  |  |  | 
Store2 |  |  |  |  |  |  | 
Cycle 1
LD1 – Issue
ADD1a – Issue
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 |  |  |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 |  |  |  |  | (R2) = 6
1 | SD R2, 0(R1) |  |  |  |  |  | Mem[100] = 6
1 | DADDIU R1, R1, #8 |  |  |  |  |  | (R1) = 108
1 | BNE R2, R3, LOOP |  |  |  |  |  | 6 ≠ 10
2 | LD R2, 0(R1) |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  | 7 ≠ 10
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 5
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 | 1 | ADD |  | 1 | Load1 |  | 
Add2 | 1 | ADD | 100 | 8 |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 |  |  |  |  |  |  | 
Load1 | 1 | LD | 100 |  |  |  | 100
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Store1 | 1 | SD | 100 |  |  | Add1 | 0
Store2 |  |  |  |  |  |  | 
Cycle 2
LD1 – Calc. Addr.
ADD1a – Wait for R2 (LD1)
SD1 – Issue
ADD1b – Issue
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 |  |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 |  |  |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 |  |  |  |  | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 |  |  |  |  | (R1) = 108
1 | BNE R2, R3, LOOP |  |  |  |  |  | 6 ≠ 10
2 | LD R2, 0(R1) |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  | 7 ≠ 10
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 6
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 | 1 | ADD |  | 1 | Load1 |  | 
Add2 | 1 | ADD | 100 | 8 |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 | 1 | BNE |  | 10 | Add1 |  | 
Br2 |  |  |  |  |  |  | 
Load1 | 1 | LD | 100 |  |  |  | 100
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Store1 | 1 | SD | 100 |  |  | Add1 | 100
Store2 |  |  |  |  |  |  | 
Cycle 3
LD1 – Load from Mem.
ADD1a – Wait for R2 (LD1)
SD1 – Calc. Addr.
ADD1b – Execute
BNE1 - Issue
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 |  |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 |  |  |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  |  | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 |  |  |  |  | 6 ≠ 10
2 | LD R2, 0(R1) |  |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 |  |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  | 7 ≠ 10
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 7
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 | 1 | ADD | 5 | 1 |  |  | 
Add2 | 0 | ADD | 100 | 8 |  |  | 
Add3 | 1 | ADD |  | 1 | Load2 |  | 
Br1 | 1 | BNE |  | 10 | Add1 |  | 
Br2 |  |  |  |  |  |  | 
Load1 | 0 | LD | 100 |  |  |  | 100
Load2 | 1 | LD | 108 |  |  |  | 0
Load3 |  |  |  |  |  |  | 
Store1 | 1 | SD | 100 |  |  | Add1 | 100
Store2 |  |  |  |  |  |  | 
Cycle 4
LD1 – Write to CDB
ADD1a – Wait for R2 (LD1)
SD1 – Wait for R2 (ADD1a)
ADD1b – Write to CDB
BNE1 – Wait for R2 (ADD1a)
LD2 – Issue
ADD2a - Issue
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 |  |  |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 |  |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 |  |  |  |  | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  |  | (R2) = 7
2 | SD R2, 0(R1) |  |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 |  |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  | 7 ≠ 10
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 8
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 | 1 | ADD | 5 | 1 |  |  | 
Add2 | 1 | ADD | 108 | 8 |  |  | 
Add3 | 1 | ADD |  | 1 | Load2 |  | 
Br1 | 1 | BNE |  | 10 | Add1 |  | 
Br2 |  |  |  |  |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 | 1 | LD | 108 |  |  |  | 0
Load3 |  |  |  |  |  |  | 
Store1 | 1 | SD | 100 |  |  | Add1 | 100
Store2 | 1 | SD | 108 |  |  | Add3 | 0
Cycle 5
ADD1a – Execute
SD1 – Wait for R2 (ADD1a)
BNE1 – Wait for R2 (ADD1a)
LD2 – Wait for BNE1
ADD2a – Wait for R2 (LD2)
SD2 – Issue
ADD2b – Issue
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  |  | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 |  |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 |  |  |  | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 |  |  |  |  | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 |  |  |  |  | (R1) = 116
2 | BNE R2, R3, LOOP |  |  |  |  |  | 7 ≠ 10
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 9
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 | 0 | ADD | 5 | 1 |  |  | 
Add2 | 1 | ADD | 108 | 8 |  |  | 
Add3 | 1 | ADD |  | 1 | Load2 |  | 
Br1 | 1 | BNE | 6 | 10 |  |  | 
Br2 | 1 | BNE |  | 10 | Add3 |  | 
Load1 |  |  |  |  |  |  | 
Load2 | 1 | LD | 108 |  |  |  | 0
Load3 |  |  |  |  |  |  | 
Store1 | 1 | SD | 100 | 6 |  |  | 100
Store2 | 1 | SD | 108 |  |  | Add3 | 0
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 |  |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 |  |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 |  |  |  | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 |  |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 |  |  |  | Wait for BNE | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  |  | 7 ≠ 10
Cycle 6
ADD1a – Write to CDB
SD1 – Wait for R2 (ADD1a)
BNE1 – Wait for R2 (ADD1a)
LD2 – Wait for BNE1
ADD2a – Wait for R2 (LD2)
SD2 – Wait for R2 (ADD2a)
ADD2b – Wait for BNE1
BNE2 - Issue
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 10
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 | 1 | ADD | 108 | 8 |  |  | 
Add3 | 1 | ADD |  | 1 | Load2 |  | 
Br1 | 0 | BNE | 6 | 10 |  |  | 
Br2 | 1 | BNE |  | 10 | Add3 |  | 
Load1 |  |  |  |  |  |  | 
Load2 | 1 | LD | 108 |  |  |  | 0
Load3 |  |  |  |  |  |  | 
Store1 | 0 | SD | 100 | 6 |  |  | 100
Store2 | 1 | SD | 108 |  |  | Add3 | 0
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 | 7 |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 |  |  |  | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 |  |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 |  |  |  | Wait for BNE | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  | Wait for R2 (ADD) | 7 ≠ 10
Cycle 7
SD1 – Write to Mem
BNE1 – Calc. Condition
LD2 – Wait for BNE1
ADD2a – Wait for R2 (LD2)
SD2 – Wait for R2 (ADD2a)
ADD2b – Wait for BNE1
BNE2 – Wait for R2 (ADD2a)
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 11
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 | 1 | ADD | 108 | 8 |  |  | 
Add3 | 1 | ADD |  | 1 | Load2 |  | 
Br1 |  |  |  |  |  |  | 
Br2 | 1 | BNE |  | 10 | Add3 |  | 
Load1 |  |  |  |  |  |  | 
Load2 | 1 | LD | 108 |  |  |  | 108
Load3 |  |  |  |  |  |  | 
Store1 |  |  |  |  |  |  | 
Store2 | 1 | SD | 108 |  |  | Add3 | 0
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 | 7 |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 8 |  |  | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 |  |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 8 |  |  | Wait for BNE | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  | Wait for R2 (ADD) | 7 ≠ 10
Cycle 8
LD2 – Addr. Calc.
ADD2a – Wait for R2 (LD2)
SD2 – Wait for R2 (ADD2a)
ADD2b – Exec
BNE2 – Wait for R2 (ADD2a)
Note: SD2 is also ready to calc addr,
But structural hazard exist w/ LD2
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 12
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 | 0 | ADD | 108 | 8 |  |  | 
Add3 | 1 | ADD |  | 1 | Load2 |  | 
Br1 |  |  |  |  |  |  | 
Br2 | 1 | BNE |  | 10 | Add3 |  | 
Load1 |  |  |  |  |  |  | 
Load2 | 1 | LD | 108 |  |  |  | 108
Load3 |  |  |  |  |  |  | 
Store1 |  |  |  |  |  |  | 
Store2 | 1 | SD | 108 |  |  | Add3 | 108
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 | 7 |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 8 | 9 |  | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 9 |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 8 |  | 9 | Wait for BNE | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  | Wait for R2 (ADD) | 7 ≠ 10
Cycle 9
LD2 – Load from Mem
ADD2a – Wait for R2 (LD2)
SD2 – Addr. Calc.
ADD2b – Write to CDB
BNE2 – Wait for R2 (ADD2a)
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 13
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 | 1 | ADD | 6 | 1 |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 | 1 | BNE |  | 10 | Add3 |  | 
Load1 |  |  |  |  |  |  | 
Load2 | 0 | LD | 108 |  |  |  | 108
Load3 |  |  |  |  |  |  | 
Store1 |  |  |  |  |  |  | 
Store2 | 1 | SD | 108 |  |  | Add3 | 108
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 | 7 |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 8 | 9 | 10 | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 |  |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 9 |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 8 |  | 9 | Wait for BNE | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  | Wait for R2 (ADD) | 7 ≠ 10
Cycle 10
LD2 – Write to CDB
ADD2a – Wait for R2 (LD2)
SD2 – Wait for R2 (ADD2a)
BNE2 – Wait for R2 (ADD2a)
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 14
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 | 1 | ADD | 6 | 1 |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 | 1 | BNE |  | 10 | Add3 |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Store1 |  |  |  |  |  |  | 
Store2 | 1 | SD | 108 |  |  | Add3 | 108
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 | 7 |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 8 | 9 | 10 | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 | 11 |  |  | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 9 |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 8 |  | 9 | Wait for BNE | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  | Wait for R2 (ADD) | 7 ≠ 10
Cycle 11
ADD2a – Exec
SD2 – Wait for R2 (ADD2a)
BNE2 – Wait for R2 (ADD2a)
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 15
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 | 0 | ADD | 6 | 1 |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 | 1 | BNE | 7 | 10 |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Store1 |  |  |  |  |  |  | 
Store2 | 1 | SD | 108 | 7 |  |  | 108
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 | 7 |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 8 | 9 | 10 | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 | 11 |  | 12 | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 9 |  |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 8 |  | 9 | Wait for BNE | (R1) = 116
2 | BNE R2, R3, LOOP | 6 |  |  |  | Wait for R2 (ADD) | 7 ≠ 10
Cycle 12
ADD2a – Write to CDB
SD2 – Wait for R2 (ADD2a)
BNE2 – Wait for R2 (ADD2a)
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6

## Slide 16
 | Busy | Op | Vj | Vk | Qj | Qk | Addr
Add1 |  |  |  |  |  |  | 
Add2 |  |  |  |  |  |  | 
Add3 |  |  |  |  |  |  | 
Br1 |  |  |  |  |  |  | 
Br2 | 1 | BNE | 7 | 10 |  |  | 
Load1 |  |  |  |  |  |  | 
Load2 |  |  |  |  |  |  | 
Load3 |  |  |  |  |  |  | 
Store1 |  |  |  |  |  |  | 
Store2 | 1 | SD | 108 | 7 |  |  | 108
Iter | Instruction | Issue @ | Exec @ | Mem access @ | Wrt. CDB @ | Comment | 
1 | LD R2, 0(R1) | 1 | 2 | 3 | 4 |  | (R2) = 5
1 | DADDIU R2, R2, #1 | 1 | 5 |  | 6 | Wait for R2 (LD) | (R2) = 6
1 | SD R2, 0(R1) | 2 | 3 | 7 |  | Wait for R2 (ADD) | Mem[100] = 6
1 | DADDIU R1, R1, #8 | 2 | 3 |  | 4 | Exec. directly | (R1) = 108
1 | BNE R2, R3, LOOP | 3 | 7 |  |  | Wait for R2 (ADD) | 6 ≠ 10
2 | LD R2, 0(R1) | 4 | 8 | 9 | 10 | Wait for BNE | (R2) = 6
2 | DADDIU R2, R2, #1 | 4 | 11 |  | 12 | Wait for R2 (LD) | (R2) = 7
2 | SD R2, 0(R1) | 5 | 9 | 13 |  | Wait for R2 (ADD) | Mem[108] = 7
2 | DADDIU R1, R1, #8 | 5 | 8 |  | 9 | Wait for BNE | (R1) = 116
2 | BNE R2, R3, LOOP | 6 | 13 |  |  | Wait for R2 (ADD) | 7 ≠ 10
Cycle 13
SD2 – Store to Mem
BNE2 – Calc. Condition
Assume: (R1) = 100, (R3) = 10, Mem[100] = 5, Mem[108] = 6